## Slide 1
Modeling and Parallel Simulation of Multicore Architectures with Manifold
The Manifold Team
School of Electrical and Computer Engineering and School of Computer Science
Georgia Institute of Technology
Atlanta, GA. 30332
Sponsors
Notes: 1

## Slide 2: Motivation
Box, G. E. P., and Draper, N. R., (1987), Empirical Model Building and Response Surfaces, John Wiley & Sons, New York, NY.
“Remember that all models are wrong; the practical question is how wrong do they have to be to not be useful.”
George E. P. Box, 2011
George E. P. Box, 2011

## Slide 3: Manifold@GT
Faculty
  Tom Conte (SCS)
  George Riley (ECE)
  S. Yalamanchili (ECE)
Research Staff
  Jun Wang (ECE)
Collaborators
  Genie Hsieh (Sandia)
  Saibal Mukhopadhyay (ECE)
  Hyesoon Kim (SCS)
  Arun Rodrigues (Sandia)
Graduate Students
  Jesse Beu
  Rishiraj Bheda
  Zhenjiang Dong
  Chad Kersey
  Elizabeth Lynch
  Jason Poovey
  Mitchelle Rasquinha
  William Song
  He Xiao
  Peng Xu
  …+ many other contributors
3

## Slide 4: Modeling and Simulation Demands
Shanghai: Quad Core
Pentium: single core
GTX200: 240 cores
Cray XT3
Scope
Complexity
System complexity is outpacing simulation capacity
  Cannot perform analysis at scale
The problem is getting worse faster  Simulation Wall
Today - islands of simulators and simulation systems
  Customized interactions
  Difficult to leverage individual investments
Power
Thermal
Packaging
Tilera: 100 cores
4

## Slide 5: Spectrum of Solutions
Leverage mature point tools via standardized API for common services
  Event management, time management, synchronization
  Learn from the PDES community
Cull the design space prior to committing to hardware prototyping or hardware acceleration strategies
Software simulations: single processor
(e.g., GEM5)
Custom Prototyping
FPGA-Based Prototyping
(e.g., RAMP)
Accelerated Simulation
(e.g., FAST)
Software Simulation: Parallel
(e.g., Manifold, COTSon)
Highest performance
Highest cost
Lowest performance
Lowest cost
Simple Premise: Use parallel machines to simulate/emulate parallel machines
5

## Slide 6: Manifold: The Big Picture
A composable parallel simulation system for heterogeneous, many core systems.
Component-based and extensible
Mixed discrete event and time stepped simulation
From full system HW/SW models to abstract timing models
From detailed cycle-level to high level analytic models
Integration of third party tools
0
0.05
0.1
0.15
0.2
0.25
0.3
0.2
0.25
0.3
0.35
0.4
time [sec]
dynamic power [W]
bzip2-program
gromacs
milc
Manifold Kernel
Manifold Kernel
Component
Component
Inter-Kernel API
Logical Process (LP)
Component
Link
Component
Component Timing/Functional Models
Parallel Simulation Kernel
Parallel Hardware Test-bed
Energy
Power
Thermal
Reliability
Models
Core degradation
Physical Models
www.manifold.gatech.edu

## Slide 7: A Typical Single OS Domain Model
Single Socket/Board model  scaling across multiple sockets
Similar efforts: Graphite, GEM5/SST, Sniper, etc.
7
CPU
L1$
L2$
CPU
L1$
R
router
CPU
L1$
L2$
CPU
L1$
R
router
CPU
L1$
L2$
CPU
L1$
R
router
Applications
Linux
PSK
PSK
PSK
VC
LP
Logical Process (LP)
LP
VC
VC
QSim
Virtual Core
Parallel Simulation Kernel (PSK)
Physical phenomena

## Slide 8: Simulation Infrastructure Challenges
Scalability
  Processors are parallel and tools are not  not sustainable
Multi-disciplinary
  Functional + Timing + Physical models
Need to model complete systems
  Cores, networks, memories, software at scale
Islands of expertise
  Ability to integrate point tools  best of breed models
Composability
  Easily construct the simulator you need
Microarch Simulator
Physical Models (power, thermal, etc.)
Applications & OS
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile

## Slide 9: Goal
Not to provide a simulator, but
Make it easy to construct a validated simulator at the fidelity and scale you want, and
Provide base library of components to build useful multicore simulators
Novel Cooling Technology
Thermal Field Modeling
Power Distr. Network
Power Management
μarchitecture
Algorithms
Microarchitecture
and Workload Execution
Power Dissipation
Thermal Coupling
and Cooling
Degradation
and Recovery

## Slide 10: Tutorial Schedule
 | Topical Description
15 minutes | Introduction and Overview
30 minutes | Execution Model and Software Organization
90 min | Component Models
15 minutes | Break
30 minutes | Building and Running Simulations
45 minutes | Energy Introspector: Integration of Physical Models
15 minutes | Some Example Simulators

## Slide 11: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 12: Manifold Execution Model and System Architecture
Execution model
Software architecture
Simulation kernel
Manifold component
Building system models

## Slide 13: Manifold Overview
A parallel simulation framework for multicore architectures
Consists of:
  A parallel simulation kernel
  A (growing) set of architectural components
  Integration of physical models for energy, thermal, power, and so on
Goal: easy construction of parallel simulators of multicore architectures
core
caches
core
caches
core
caches
core
caches
Interconnection network
memory
controller
memory
controller
Ease of composition
cache
cache
cache
core
core
core
kernel
network
network
network
memory
memory
memory
other
other
other
Manifold repository

## Slide 14: Execution Model: Overview
Instruction stream
  Generated by i) trace files, ii) Qsim server, iii) Qsim Lib
System timing model
  Multicore model built with Manifold components
  Components assigned to multiple logical processes (LPs)
    Each LP assigned to one MPI task; LPs run in parallel
Instruction stream
System timing model
Traces
Serial Emulator
Parallel Emulator
Options
Cycle level components
High level timing components
Physical Models (e.g., Power)
backpressure

## Slide 15: Execution Model: Software Organization
Manifold Kernel
Manifold Kernel
Physical Core 0
Physical Core 1
Component
Component
Component
Component
Kernel – Component API
Inter-Kernel API
Component models connected to form system models
Full system emulation front-end
All time management is handled by the simulation kernel
APIs  key to integrating mature point tools
Logical Process (LP)
Logical Process (LP)
Component
Inter-component API
QSim Client/Server Emulator
15
Instruction streams

## Slide 16: An Example System Model
Multicore SMP system
Core, cache, memory controller models each represented by a Manifold component
Network contains multiple components: interfaces, routers
core
caches
core
caches
core
caches
core
caches
Interconnection network
memory
controller
memory
controller
Manifold
component
Manifold
component
multiple Manifold
components

## Slide 17: Execution Model
Timing-directed full-system simulation
Front-end performs functional emulation; timeless
Back-end for timing simulation
Front-end is regulated by back-end
Qsim
proxy
Qsim
proxy
application
Linux
VCPU
Virtual CPU
VCPU
VCPU
core
L1$
L2$
PSK
core
L1$
L2$
PSK
core
L1$
L2$
network
MPI
PSK
PSK
logical process (LP)
LP
LP
LP
Functional
front-end
Timing
back-end
TCP/IP
shared memory
QSim

## Slide 18: Manifold Execution Model and System Architecture
Execution model
Software architecture
Simulation kernel
Manifold component
Building system models

## Slide 19: Software Architecture (1/2)
Layered architecture
Standardized component interfaces
Goal:
  Encapsulation of parallel-discrete event simulation functionality
  Allow components to evolve independently
  plug-n-play construction of simulators
simulation kernel
core
model
network
model
memory
model
user
model
cache
model
models (components)
cross-model
simulator

## Slide 20: Software Architecture (2/2)
Standardized component interfaces
  allows components to be independent of each other: no compile-time dependence
  allows components to be interchangeable
Example
  processor-cache interface
cache
model
core model 1
core model 2
cache
model
core model 1
simulator
cache
model
core model 2
simulator
library

## Slide 21: Source Code Organization
How to get the code?
  Distribution package: http://manifold.gatech.edu/download
  SVN: https://svn.ece.gatech.edu/repos/Manifold/trunk
code
|... doc
|... kernel
|... models
| |... cache
| |... cross
| |... energy_introspector
| |... memory
| |... network
| |... processor
|... simulator
|... uarch (common micro-architecture classes)
|... util (utility programs)

## Slide 22: Manifold Execution Model and System Architecture
Execution model
Software architecture
Simulation kernel
Manifold component
Building system models

## Slide 23: Simulation Kernel (1/2)
Simulation Kernel
  provides facilities for creating / connecting components
  provides clock related functionalities
  Encapsulates parallel discrete-event simulation (PDES) services
    Transparent synchronization between parallel LPs
    All event management
Qsim
proxy
Qsim
proxy
application
Linux
VCPU
Virtual CPU
VCPU
VCPU
core
L1$
L2$
PSK
core
L1$
L2$
PSK
core
L1$
L2$
network
MPI
PSK
PSK
logical process (LP)
LP
LP
LP
Functional
front-end
Timing
back-end
TCP/IP
shared memory
QSim

## Slide 24: Simulation Kernel (2/2)
Interface
  Component functions
    create / connect components
    send output
  Clock functions
    create clocks
    register component with clock
    Support for dynamic voltage frequency scaling (DVFS)
  Simulation functions
    start / stop simulation
    statistics
Encapsulated part
  PDES engine: event management, event handling, inter-process communication, synchronization algorithms

## Slide 25: Manifold Execution Model and System Architecture
Execution model
Software architecture
Simulation kernel
Manifold component
Building system models

## Slide 26: Operational Model of a Component (1/3)
Component is connected to other components via links
For each input port, there should be an event handler
Can register one or two functions with a clock; registered functions are called every clock cycle
For output, use Send()
  Paradigm shift: OO event-driven
    Instead of comp->function(data), call Send(data)
    No method invocation: comp->function()
    May not even have a valid pointer: component could be in another process
  Kernel ensures receiver’s handler is called at the right moment
event_handler(T*)
Send(Data*)
rising() / falling()
component
component

## Slide 27: Operational Model of a Component (2/3)
How is the event handler of component invoked?
Example: component c1 sends data at cycle t to component c2; link delay is d cycles
  What’s expected: c2’s handler is called at cycle (t+d)
Case 1: c1 and c2 in same LP
  When c1 is connected to c2, a LinkOutput object is created that holds a pointer to c2, and a pointer to its handler.
  When c1’s Send() is called, the LinkOutput object calls kernel’s schedule function to schedule an event that calls c2’s handler at (t+d).
c1
c2
kernel
LP

## Slide 28: Operational Model of a Component (2/3)
Case 2: c1 and c2 in different LPs
  When c1 is connected to c2, a LinkInput object for c2 is created that holds a pointer to its handler.
  When c1’s Send() is called, kernel1 sends data to kernel2, which passes it to c2’s LinkInput object, which calls kernel2’s schedule function to schedule an event that calls c2’s handler at (t+d).
The same Send() function is used in both cases!
LP2
c1
c2
kernel
LP1
kernel

## Slide 29: Manifold Component (1/2)
Must be a subclass of manifold::kernel::Component
Must define event handlers for incoming data
Must use Send() to send outputs
Define functions for rising/falling edge if required
For more, see Manifold Component Developer's Guide
class MyComponent : public manifold::kernel::Component
{
public:
enum {PORT0=0, PORT1};
void handler0(int, MyDataType0*);
void handler1(int, MyDataType1*);
void rising();
void falling();
};

## Slide 30: Manifold Component (2/2)
Important functions in manifold::kernel::Component
Create()
  create a component
  5 overloaded template functions
Send()
  send data out of a port to a component connected to the port
  no recv() function: incoming events handled by event handler.
template<typename T, typename T1)
void Create(int, T1, CompName);
template<typename T>
void Send(int, T);

## Slide 31: Manifold Execution Model and System Architecture
Execution model
Software architecture
Simulation kernel
Manifold component
Building system models

## Slide 32: Building System Models and Simulation Programs (1/2)
Steps for building a simulation program
  Initialization
  Build system model (see next slide)
  Set simulation stop time
  Start simulation
  Finalization
  Print out statistics

## Slide 33: Building System Models and Simulation Programs (2/2)
Building a system model
  Create clock(s) (call constructor)
  Create components (call Component::Create())
  Connect components (call Manifold::Connect())
  Register clock-driven components with clock, if not already registered. (call Clock::Register())

## Slide 34: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 35
QSim1: Overview
  Thread safe multicore x86 emulation library using QEMU2
    C++ API for instantiating, controlling, and instrumenting emulated CPUs
  Guest environment runs:
    Lightly modified Linux kernel
    Unmodified 32-bit x86 binaries
  Instruction-level execution control
  Instruction-level instrumentation
  Qsimlib : for creating multithreaded emulators
  QSimServer: for serving parallel/distributed simulations
2F. Bellard, “QEMU Open Source Processor Emulator,” http://www.qemu.org/
35
1C. Kersey, A. Rodrigues, and S. Yalamanchili, “ A Universal Parallel Front-End for Execution-Driven Microarchitecture Simulation,” HIPEAC Workshop on Rapid Simulation and Performance Evaluation: Methods and Tools, January 2012

## Slide 36
QSim Architecture: QEMU Core
  Emulation performed through dynamic binary translation.
  Code from translation cache can call helper functions
    Instrument code cache
  QSim's QEMU CPU library uses external Guest RAM state.
    Allows sharing between multiple instances
  Synchronization allows multiple ordinary QEMU CPUs or a single QEMU CPU performing an atomic memory operation to run.
QEMU Core
36

## Slide 37
QSim Architecture: Timing Model Interface
  Instrumentation of the translation cache
  Timing model feedback – backpressure from hardware events
  Synchronized advance of functional and timing models rather than roll-back and recovery
  Memory and instruction information

## Slide 38
QSim Multicore Emulator
Functional front-end for microarchitecture simulation
  Runs unmodified x86 (32-bit) binaries on lightly-modified Linux kernel.
  Provides callback interface for execution events
  Callbacks generated for all instructions, including OS
  Optional callbacks for instruction read during translation
    Support for distributed memory.
Based on QEMU dynamic binary translator
Inserts calls to callback functions into translation cache
Adds support for precise instruction counting
  User-mode threading
Notes: 38

## Slide 39
How it Works: Block Diagram

## Slide 40
Getting, Building, and Installing QSim
Latest version supported by Zesto core model and remote API:
http://www.cdkersey.com/qsim-web/releases/qsim-0.1.5.tar.bz2
Latest release (preferred for new core models):
https://github.com/cdkersey/qsim/archive/0.2.1.tar.gz
Current development tree (API is stable):
https://github.com/cdkersey/qsim
INSTALL file in source tree: step-by-step installation instructions.
Benchmarks (pre-compiled applications) at:
http://www.cdkersey.com/qsim-web/releases/qsim-benchmarks-0.1.1.tar.bz2

## Slide 42
Using QSim: Application Requirements
Applications must be:
  Linux ELF Binaries
  All libraries included
  All required input data included
  Most included benchmarks statically linked
qsim-load expects a .tar file with a runme.sh
  $NCPUS is the number of emulated HW threads
fmm/runme.sh
#!/sbin/ash
echo $NCPUS > ncpus
cat input.top \
ncpus input.bot \
> input
./FMM < input
barnes/runme.sh
#!/sbin/ash
echo $NCPUS >> input
./BARNES < input
radiosity/runme.sh
#!/sbin/ash
./RADIOSITY \
-ae 5000.0 \
-en 0.050 \
-bf 0.10 \
-batch -room \
-p $NCPUS

## Slide 43
Using QSim: Saved States
OS Boot for large number of CPUs takes a long time even at high (~10MIPS) simulation speeds
Use state files to checkpoint already-booted CPU state
mkstate.sh script for generating state files.
  Script that runs qsim-fastforwarder program

## Slide 45
Using QSim: Application Start/End Markers
Need to mark "region of interest" in applications.
This is done through "magic" instructions.
CPUID instruction with special register values:
  %rax = 0xaaaaaaaa for application start
  %rax = 0xfa11dead for application end
#ifdef QSIM
#define APP_START() do { \
__asm__ __volatile__("cpuid;"::"a"(0xaaaaaaaa));\
} while(0)
#define APP_END() do { \
__asm__ __volatile__("cpuid;"::"a"(0xfa11dead));\
} while(0)
#endif

## Slide 46
Using QSim: Applications and the OS
"Emulates all OS instructions" means exactly that:
  Timer interrupts are necessary and the scheduler does run.
  Quite a bit lot of time is spent handling page faults.
Can query and filter out OS instructions if they are considered irrelevant:
  OSDomain::getProt(core) == OSDomain::PROT_KERNEL

## Slide 47
QSim Remote API: The Server and Proxy
A subset of the QSim API is provided for operation over a network.
Server performs functional simulation; client performs timing model.
Client API looks like QSim API:
One thread per client.
Proxy acts as intermediary between clients and server.
  Third program that hides network latency.
  Necessary because client library uses blocking I/O.

## Slide 49
QSim API: Basic Functionality
OSDomain Func. | Purpose
get_prot(core) | Get protection level (KERN, USER)
get_idle(core) | Is the core running the kernel idle loop?
run(core, n) | Run the selected core for n instructions.
timer_interrupt() | Interrupt all CPUs. (required)
Callback Setters | 
set_mem_callback(obj, f) | Memory accesses (loads, stores)
set_atomic_callback(obj, f) | Atomic read/modify/write operations
set_inst_callback(obj, f) | All instructions
set_reg_callback(obj, f) | Register reads/writes
set_int_callback(obj, f) | Interrupts, including exceptions
set_trans_callback(obj, f) | Reads into QEmu translation cache
set_app_start_callback(obj, f) | Beginning of application (start marker)
set_app_end_callback(obj, f) | End of application (end marker)
For full details, including callback prototypes, see user guide.

## Slide 50
QSim API: Timer Interrupt
Information about time not communicated back to QSim from the timing model.
  Periodic interrupts simulating PIT events are the only timing information that reaches the OS.
  OSDomain::timer_interrupt() must be called periodically (~1-10ms to sim time) for the entire OSDomain
Not setting the timer interrupt leads to scheduled threads never running.

## Slide 51
QSim API: Simple Sample Program
class TraceWriter
{private: OSDomain &osd; ostream &trf;
public: bool done;
TraceWriter(OSDomain &osd, ostream &trf) :
osd(osd), trf(trf), done(false)
{ osd.set_inst_cb(this, &TraceWriter::inst_cb);
osd.set_app_end_cb(this, &TraceWriter::app_end_cb); }
void inst_cb(int c, uint64_t v, uint64_t p, uint8_t l,
const uint8_t *b, enum inst_type t)
{ trf << std::dec << c << ',' << v << ',' << p << ',' << t << endl; }
int app_end_cb(int c) { done = true; return 1; } };
int main(int argc, char** argv)
{ ofstream trace(argv[3]); // Arg 3 : trace file
OSDomain osd(argv[1]); // Arg 1 : state file
load_file(osd, argv[2]); // Arg 2 : benchmark
TraceWriter tw(osd, trace);
while (!tw.done)
{ for (unsigned i = 0; i < 100; ++i)
for (unsigned j = 0; j < osd.get_n(); ++j)
osd.run(j, 10000);
osd.timer_interrupt(); }
trace.close();
return 0; }

## Slide 52: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 53
Additional Slides

## Slide 54
How it Works: Lock Table
QSim is a thread-safe library.
Each simulated CPU is a QEmu instance.
RAM state is shared.
Memory has readers/writer lock semantics
  1 thread executing an atomic OR
  any number of threads executing ordinary memory operations
This can be applied on a per-address basis
We build a table of spinlocks
  Spinlock code appropriated from Linux kernel.

## Slide 55: Back-end Timing Models
Core Models
Interconnection Network
Memory System
  Coherence Cache Hierarchy
  DRAM Controller

## Slide 56: Core Models
Zesto – cycle-level x86 processor model
SPX – a light pipe-lined model
SimpleProc – a 1-IPC model

## Slide 57: Zesto* Overview
Consists of an oracle and a detailed pipeline
Oracle is an “execution-at-fetch” functional simulator; fetched instructions are first passed to oracle
Pipeline has 5 stages
Very detailed; slow (10’s of KIPS)
Ported to Manifold as a component
*G. Loh, etc., “Zesto: a cycle-level simulator for highly detailed microarchitecture exploration,” International Symposium on Performance Analysis of Software and Systems (ISPASS), pp53-64, 2009
Oracle
(functional)
Detailed pipeline model
(superscalar / OOO pipeline)
cache
x86 instructions6
recovery info
memory requests
and replies

## Slide 58: Zesto
X86 based timing model derived from Zesto cycle-level simulator
  IA 32 support

## Slide 59: Zesto Interface
Front-end interfaces
Cache request
Event handler (for cache response)
Clocked function
Multiple instances with different front-end interfaces

## Slide 60: Zesto Interface
ZestoCacheReq
event handler for cache response
class core_t {
public:
...
void cache_response_handler(int, ZestoCacheReq*);
...
};

## Slide 61: Zesto Interface
Clocked function
  must be registered with a clock
  Zesto does not register this function, so it must be registered in the simulator program.
void core_t :: tick()
{
//get the pipeline going
commit->step();
exec->LDST_exec();
...
alloc->step();
decode->step();
fetch->step();
...
}

## Slide 62: Simplified Pipeline eXecution (SPX) <A simpler, lighter core model for out-of-order and in-order pipelines>

## Slide 63: SPX
SPX is an abbreviated core model that support both out-of-order and in-order executions.
Purpose: Detail vs. Speed
  For less core-sensitive simulations (i.e., memory/network traffic analysis), detailed core implementation may be unnecessary.
  Physics simulations need longer observation time (in real seconds) than typical architectural simulations
    e.g., temperature doesn’t change much for several hundreds million clock cycles (or several hundred milliseconds) of simulation.
The SPX model provides enough details to model out-of-order and in-order executions, and other optional behaviors are all abbreviated (e.g., predictions)
The SPX requires Qsim Library for detailed instruction information.
  Queue model is not currently supported.
  SPX uses direct Qsim callback functions.

## Slide 64: Modeled Components in SPX
InstQ: A queue that fetches the instructions from Qsim.
RF: Register file that tracks only dependency; behaves more like RAT.
  Dependency for general register files and flags are maintained.
RS: Dependency status tracker.
  It does not have an actual table like scoreboard.
  When an instruction is ready (cleared from dependency), it is put in the ReadyQ.
  In-order execution is modeled with 1-entry RS.
EX (FU): Multi-ported execution units.
  Each FU is defined with latency and issue rate.
ROB: Re-order buffer for out-of-order execution
  An instruction can be broken into multiple sub-instructions (e.g., u-ops), and ROB commits the instruction when all sub-instructions are completed.
LDQ/STQ: Load and store queues
  These queues check memory dependency between ST/LD instructions.

## Slide 65: Out-of-order Pipeline
InstQ
Qsim Lib
Callbacks
Translation to SPX instruction
ROB
RS
LDQ
STQ
Allocate if Available
RF
Allocate if Available
Allocate if LD
And Available
Allocate if ST
And Available
Resolve Dependency
Reg. Dep.
Status
EX
FU
FU
FU
FU Port Binding
Mem. Dep.
CheckWhen Allocate
Schedule
Schedule When Commit
Cache Req. After EX
Cache Req. After Commit
Update
Store Fwd
Update
Cache Resp.
Update
Writeback

## Slide 66: In-order Pipeline
InstQ
Qsim Lib
Callbacks
Translation to SPX instruction
threadQ
LDQ
STQ
RF
Allocate if Available
Allocate if LD
And Available
Allocate if ST
And Available
Resolve Dependency
Reg. Dep.
Status
EX
FU
FU
FU Port Binding
Mem. Dep.
CheckWhen Allocate
Schedule
Cache Req. After EX
Cache Req. After EX
Writeback
Store Fwd
Update
Cache Resp.
Update
Schedule

## Slide 67: SPX Interface
Front-end
Cache request
Event handler (for cache response)
Clocked function

## Slide 68: SPX Interface
cache_reqest_t
event handler for cache response
class spx_core_t {
public:
...
void handle_cache_response(int, cache_reqest_t*);
...
};
clocked function
  must be registered with a clock
  SPX does not register this function, so it must be registered in the simulator program.
void spx_core_t :: tick()
{
...
}

## Slide 69: SimpleProc
1-IPC: in general one instruction is executed every cycle
MSHR limits number of outstanding cache requests

## Slide 70: SimpleProc Interface
Front-end
Cache request
Event handler (for cache response)
Clocked function

## Slide 71: SimpleProc Interface
CacheReq
event handler for cache response
class SimpleProcessor {
public:
...
void handle_cache_response(int, CacheReq*);
...
};
clocked function
  must be registered with a clock
  SimpleProc does not register this function, so it must be registered in the simulator program.
void SimpleProcessor :: tick()
{
...
}

## Slide 72: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 73: Back-end Timing Models
Core Models
Interconnection Network
Memory System
  Coherence Cache
  DRAM Controller

## Slide 74: The Network Simulator - IRIS
Basic router/switch designed to enable design space exploration
  Ease of changing VC & switch allocators, buffering, routing function, selection functions, etc.
Topology generators for Ring and Tori
  You can write your own
74
Virtual channels
Ring and torus
Request-reply network
Single-flit and multiflit packets
Credit-based flow control
Must instantiate a network interface

## Slide 75: Iris Interface
User creates an Iris network using one of the following:
template<typename T> Ring<T>* create_ring();
template<typename T> Torus<T>* create_torus();
parameters:
  Clock& clk – clock for the network
  ring_init_params* or torus_init_params* - parameters for the ring or torus
  Terminal_to_net_mapping* - object that maps terminal address to network address
  SimulatedLen<T>* - object that computes a packet's simulated length
  VnetAssign<T>* - object that determines a packet's virtual network
  int ni_credit_type – type of credit messages between NI and terminal
  vector<int>* node_lp – LP assignment of the routers

## Slide 76: Iris Interface
NIs and routers are created internally
NIs and routers are registered to the clock internally
NIs can be accessed through get_interface_id(), or get_interfaces()
Each NI can connect to one terminal (e.g., cache)
Router is encapsulated

## Slide 77: Iris Network Interface
A template class:
  template<typename T> class GenNetworkInterface
  T is the type of packets sent to the network
Network packet interface

## Slide 78: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 79: Multi-core Systems and Coherence Hierarchies
Coherence hierarchy issues
  Several architecture specific implementations
  Design complexity
    Complex hierarchy state encodings
    Many more transient states
Solution: Coherence Realm* Encapsulation
  Define communication interface between users and monitors
  Enables layering of coherence
  Enables heterogeneity within a protocol

## Slide 80: Manager-Client Pairing (MCP)*
*J. G. Beu, M. C. Rosier and T. M. Conte, “Manager-Client Pairing: A Framework for Implementing Coherence Hierarchies,” Proceedings of the 44th Annual International Symposium on Microarchitecture (MICRO-44), (Porto Alegre, Brazil), Dec., 2011.

## Slide 81: Division of Labor
Client Agent (think cache)
  Permission holder (Coherence State)
  Obtains permission via acquire requests
  Act as a gateway in hierarchical coherence (see algorithm)
Manager Agent (think directory)
  Monitor of coherence realm
    Records sharers, owner, etc.
  Manages permission propagation
    Process acquire requests
    Allocates/de-allocates permissions to/from clients
    Handles external requests from other realms

## Slide 82: Base Functions

## Slide 83: Special Functions
Client: Eviction Permissions?
  Evict_P and GetEvict
  Why? What if in M/O state?
    Directory is making assumptions about client’s role
      That client will fwd data to other caches
    Client needs to inform directory before giving up ownership
Manager: Downgrade (DwnInval and DwnRead)
  Realm A has in the M state
  Realm B asks for permission
    Asks for write permission, A needs to become invalid
    Asks for read permission, A only needs to give up exclusivity but can keep a copy

## Slide 84: Permission Hierarchy Algorithm

## Slide 85: Example – Realm Read Hit

## Slide 86: Example – Realm Write Miss

## Slide 87: Cache Model and Interface
A cache model has two interfaces:
The processor-cache interface and
The cache-network interface.
The Processor-Cache Interface
On the process-cache interface, the processor sends requests to the cache and the cache sends responds back.
Message from processor
The processor model's request is supposed to implement the following two functions:
1. get_addr(). This function returns a 64-bit integer that is the memory address for which the cache request is made.
2. is_read(). This function returns true if the request is a read(load), and false if it is a write(store).
The cache model's event handler for the processor-cache interface should be a templated function similar to the following:
template<typename T>
void my_cache_req_handler(int, T*);
The templated type T is the type of the request from the processor.
Message to processor
Currently it is required that the cache model sends back to the processor the same data type that it gets from the processor. Therefore, if the processor sends type T to the cache, then the cache must respond with the same type T.

## Slide 88: Cache-Network Interface
If the cache model is not directly connected to the interconnection network, it can send/receive its own data type. If it is connected to the network, then it should send/receive manifold::uarch::NetworkPacket
The cache model's own data should be serialized and stored in the member variable (an array) data of NetworkPacket. The simplest way to do this is just using byte-wise copy:
MyDataType* obj;
NetworkPacket* pkt = new NetworkPacket();
*((MyDataType*)pkt->data) = obj;
A cache model could send two types of messages over the network:
1. Cache-to-cache messages, such as coherence messages.
2. Cache-to-memory messages.
Both are carried by NetworkPacket.

## Slide 89: Cache-Network Interface….
A cache model also receives two types of messages: from another cache or from memory. The event handler for its network input should be a templated function as follows:
template<typename T>
void my_net_handler(int, manifold::uarch::NetworkPacket*);
where the template parameter T is the data type from memory controller and is supposed to define the following two functions:
get_addr(). This functions returns a 64-bit integer that is the memory address for which the cache request is made.
is_read(). This function returns true if the request is a read(load), and false if it is a write(store). Pseudo code for the cache model's event handler for the cache-network interface is given below:
template<typename T>
void my_net_handler(int, manifold::uarch::NetworkPacket* pkt)
{
IF pkt->type == coherence message THEN
MyCohMsg* coh = new MyCohMsg();
*coh = *((MyCohMsg*)(pkt->data));
process(coh);
ELSE IF pkt->type == memory message THEN
T objT = *((T*)(pkt->data));
MyMemMsg* mem = new MyMemMsg;
Set the member values of mem with objT;
process(mem);
END IF
}

## Slide 90: CaffDRAM Overview
Processor
Cache
Integrated DDRx Memory Controller
Memory Bus
Memory System
CaffDRAM is a cycle accurate DRAM timing simulator. This simulator is JEDEC compliant and models various timing parameters pertaining to resource contention within the DRAM main memory.

## Slide 91: Memory Organization
Memory Controller
CH 1
CH2
CH N
RANK 1
RANK 2
RANK 3
RANK 4
*A Single DIMM Module may consist of “one” or “two” Ranks depending upon its pin configuration. Each Side of a DIMM module is one “RANK” . A single “RANK” usually consists of 8 “x8” chips corresponding to a Data Bus width of 64 bits

## Slide 92: DRAM Scheduling
Command Generator
Channel Bus Scheduler
Rank Scheduler
Bank Scheduler
Request Queue
DRAM Policies
Delay Parameters
DRAM Configuration
SPD
(Serial Presence Detect)
Incoming
Request

## Slide 93: Rank I/O Devices Contention Modeling
Rank I/O Device
* On every “Read” multiple internal bursts are required to form a Longer burst on the data bus.
* On every “Write” data direction is reversed and these devices act as buffers for incoming data.
I/O Devices in use = Busy for “t_CCD” cycles
t_CCD = 2 beats for DDR = 1 memory cycle
t_CCD = 4 beats for DDR2 = 2 memory cycles
t_CCD = 8 beats for DDR3 = 4 memory cycles
Rank Scheduler responsible for “I/O Device” resource contention
Single Rank

## Slide 94: Bank Contention Modeling
An Active Row
Sense Amplifiers
(Each Bank has a set of sense Amplifiers
shared by each row in a bank)
A Bank when accessed on a memory request
activates a row which fills in the “sense amplifiers”
with data from that row
This operation takes time = t_RCD
After time t_RCD, data from the “addressed columns”
may be accessed.
After time = t_CAS (a.k.a. t_CL) data is placed on
the Channel Data Bus
Bank Scheduler responsible for “Multiple Row Conflict”
within a bank

## Slide 95: Bank Contention Modeling….
Previously Active Row
Newly accessed row within same bank
causing resource conflict
Row Activation = Bank busy for “t_RAS” cycles
Bank Precharge = Bank busy for “t_RP” cycles
*If a subsequent access is made to the same open row, the request can proceed
immediately after the first without having to wait for t_RAS. In case of a different row
the timing protocol must be followed

## Slide 96: CaffDRAM Interface
* A memory controller has one interface: the memory controller-network interface. It sends/receives NetworkPacket which carries the memory requests and responses.
* The requests are defined in the cache model, therefore, the memory controller does not have the definition. For this reason, the event handler should be a template function as follows:
template<typename T>
void handler(int, manifold::uarch::NetworkPacket* pkt)
{
T* request = (T*)(pkt->data);
bool isRead = request->is_read();
uint64_t addr = request->get_addr();
...
}

## Slide 97: CaffDRAM Interface….
As can be seen, the request from cache is supposed to implement the following two functions:
get_addr(). This functions returns a 64-bit integer that is the memory address for which the cache request is made.
is_read(). This function returns true if the request is a read(load), and false if it is a write(store).
For response, the memory controller model can reuse the data type of the cache's requests, or it can define its own. In the latter case, the data type must also support the same two functions above.
Message Types
The responses sent by the memory controller model use a message type (the type filed of NetworkPacket) that should be different from other message types. Therefore, the memory controller developer should not hard code the message type value. Instead, the type should be set in the constructor or an access function. The system model builder is responsible for setting the types.

## Slide 98: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 99: Building and Running Parallel Simulations
Instantiate Components
Connect Components
Register Clocks
Simulation Functions
Initialization
Configuration parameters
From Manifold Library
Inputs (trace, QSIM, etc.)
Instantiate Links
Set Timing Behavior
Time stepped vs. discrete event
Set Duration, Cleanup, etc.

## Slide 100: Building and Running Parallel Simulations
Kernel Interface
Simulator Construction
Logs and Statistics
Demos

## Slide 101: Kernel Interface
Component functions
  create component
    component can have 0-4 constructor arguments
    template allows constructor parameters to be any type
    returns unique integer ID
Component::Create<qsimclient_core_t>(lp, node_id, m_conf, cpuid, proc_settings);
//component-decl.h
template <typename T>
static CompId_t Create(LpId_t, CompName name=CompName(“none”));
...
template <typename T, typename T1, typename T2, typename T3, typename T4>
static CompId_t Create(LpId_t, const T1&, const T2&, const T3&, const T4&, CompName name=CompName(“none”));

## Slide 102: Kernel Interface
  Connect components
    one-way connection
    two-way connection
//manifold-decl.h
template<typename T, typename T2>
static void Connect(CompId_t srcComp, int srcIdx, CompId_t dstComp, int dstIdx, void (T::*handler)(int, T2), Ticks_t latency);
//manifold-decl.h
template<typename T, typename T2, typename U, typename U2>
static void Connect(CompId_t comp1, int idx1, void (T::handler1)(int, T2), CompId_t comp2, int idx2, void(U::*handler2)(int, U2), Clock& clk1, Clock& clk2, Ticks_t latency1, Ticks_t latency2);
Source
component
Destination
component
srcIdx
dstIdx

## Slide 103: Kernel Interface
Clock functions: constructor, Register()
//clock.h
Clock(double freq);
template<typename O>
static tickObjBase* Register(Clock& clk, O* obj, void (O::*rising)(void)
void (O::*falling)(void));
simulation functions
//manifold-decl.h
static void Init(int argc, char**argv, SchedulerType=TICKED,
SyncAlg::SyncAlgType_t syncAlg=SyncAlg::SA_CMB_OPT_TICK,
Lookahead::LookaheadType_t la=Lookahead::LA_GLOBAL);
static void Finalize();
static void StopAt(Ticks_t stop);
static void Run();

## Slide 104: Simulator Construction
Steps for building a simulation program
  Call Manifold::Init()
  Build system model: Clock(); Create(), Connect(), Register()
  Set simulation stop time: StopAt()
  Call Manifold::Run()
  Call Manifold::Finalize()
  Print out statistics: print_stats()

## Slide 105: Logs and Statistics
Each component collects its own statistics
A convention for printing stats is:
  void print_stats(std::ostream&);

## Slide 106: Example Simulators
Simulator 1:
  For demo purposes only
  Builds a 2-core system
    2 Zesto cores
    MCP cache
    Iris(2x2 torus)
    CaffDRAM
  Runs sequential or parallel (3 LPs) simulation
Simulator 2:
  Part of software distribution
  3 programs: work with Qsim server, Qsim lib, and traces, respectively
  Core model can be replaced with one-line change to configure file

## Slide 107: Sample Results: Setup
16, 32, 64-core CMP models
2, 4, 8 memory controllers, respectively
5x4, 6x6, 9x8 torus, respectively
Host: Linux cluster; each node has 2 Intel Xeon X5670 6-core CPUs with 24 h/w threads
13, 22, 40 h/w threads used by the simulator on 1, 2, 3 nodes, respectively
200 Million simulated cycles in region of interest (ROI)
  Saved boot state and fast forward to ROI

## Slide 108: Sample Results: Simulation Time in Minutes
 | 16-core |  | 32-core |  | 64-core | 
 | Seq. | Para. | Seq. | Para. | Seq. | Para.
dedup | 1095.7 | 251.4 (4.4X) | 2134.8 | 301.3 (7.1X) | 2322.9 | 345.3 (6.7X)
facesim | 1259.3 | 234.9 (5.4X) | 2614.2 | 303.6 (8.6X) | 3170.2 | 342.3 (9.3X)
ferret | 1124.8 | 227.8 (4.9X) | 1777.9 | 255.6 (7.0X) | 2534.3 | 331.3 (7.6X)
freqmine | 1203.3 | 218.0 (5.5X) | 1635.6 | 245.6 (6.7X) | 2718.9 | 337.3 (8.1X)
stream | 1183.8 | 222.7 (5.3X) | 1710.6 | 244.3 (7.0X) | 4796.4 | 396.2 (12.1X)
vips | 1167.0 | 227.3 (5.1X) | 1716.3 | 257.2 (6.7X) | 2564.6 | 337.9 (7.6X)
barnes | 1039.9 | 224.3 (4.6X) | 1693.0 | 283.3 (6.0X) | 3791.8 | 341.4 (11.1X)
cholesky | 1182.4 | 227.2 (5.2X) | 1600.3 | 245.7 (6.5X) | 4278.3 | 402.1 (10.6X)
fmm | 1146.3 | 229.6 (5.0X) | 1689.8 | 253.6 (6.7X) | 5037.2 | 416.1 (12.1X)
lu | 871.2 | 156.4 (5.6X) | 1475.8 | 204.6 (7.2X) | 4540.3 | 402.7 (11.3X)
radiosity | 1022.3 | 228.8 (4.5X) | 1567.5 | 250.4 (6.3X) | 2813.5 | 350.3 (8.0X)
water | 671.5 | 158.4 (4.2X) | 1397.3 | 236.7 (5.9X) | 2560.1 | 356.3 (7.2X)

## Slide 109: Sample Results: Simulation in KIPS
 | 16-core |  | 32-core |  | 64-core | 
 | Seq. | Para. | Seq. | Para. | Seq. | Para.
dedup | 49.28 | 211.98 | 48.56 | 340.61 | 16.88 | 136.82
facesim | 58.66 | 316.42 | 47.90 | 401.72 | 30.01 | 278.94
ferret | 57.77 | 284.81 | 35.41 | 239.59 | 18.10 | 139.54
freqmine | 57.15 | 314.99 | 37.01 | 248.60 | 19.37 | 140.18
stream | 58.77 | 314.34 | 36.73 | 260.04 | 41.42 | 419.77
vips | 58.03 | 298.09 | 34.92 | 236.06 | 18.02 | 131.02
barnes | 30.66 | 151.32 | 32.62 | 168.74 | 39.61 | 219.63
cholesky | 57.95 | 301.47 | 38.87 | 254.54 | 45.68 | 491.46
fmm | 51.01 | 252.46 | 37.90 | 255.86 | 40.94 | 525.51
lu | 50.93 | 155.74 | 39.78 | 119.46 | 46.23 | 485.04
radiosity | 50.87 | 206.96 | 53.15 | 229.02 | 36.29 | 268.70
water | 27.86 | 95.81 | 29.85 | 132.22 | 25.72 | 179.88
Mean | 50.75 | 242.03 | 39.39 | 240.54 | 31.52 | 284.71
Median | 54.08 | 268.63 | 37.45 | 244.10 | 33.15 | 244.16

## Slide 110: Sample Results: KIPS per Hardware Thread
 | 16-core |  | 32-core |  | 64-core | 
 | Seq. | Para. | Seq. | Para. | Seq. | Para.
dedup | 49.28 | 16.31 | 48.56 | 15.48 | 16.88 | 3.42
facesim | 58.66 | 24.34 | 47.90 | 18.26 | 30.01 | 6.97
ferret | 57.77 | 21.91 | 35.41 | 10.89 | 18.10 | 3.49
freqmine | 57.15 | 24.23 | 37.01 | 11.30 | 19.37 | 3.50
stream | 58.77 | 24.18 | 36.73 | 11.82 | 41.42 | 10.49
vips | 58.03 | 22.93 | 34.92 | 10.73 | 18.02 | 3.28
barnes | 30.66 | 11.64 | 32.62 | 7.67 | 39.61 | 5.49
cholesky | 57.95 | 23.19 | 38.87 | 11.57 | 45.68 | 12.29
fmm | 51.01 | 19.42 | 37.90 | 11.63 | 40.94 | 13.14
lu | 50.93 | 11.98 | 39.78 | 5.43 | 46.23 | 12.13
radiosity | 50.87 | 15.92 | 53.15 | 10.41 | 36.29 | 6.72
water | 27.86 | 7.37 | 29.85 | 6.01 | 25.72 | 4.50
Mean | 50.75 | 18.62 | 39.39 | 10.93 | 31.52 | 7.12
Median | 54.08 | 20.66 | 37.45 | 11.09 | 33.15 | 6.10

## Slide 111: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 112
Energy Introspector: Integration of Physical Models

## Slide 113: Architecture-Physics Co-Simulation
Monitored Physics (Power, Temperature, etc.)
Architecture Simulations ➔ Physical phenomena
Physical Phenomena ➔ Control Algorithms
Control Algorithms ➔ Architectural Executions
Microarchitectural Simulation
(Functional Models)
Physical Phenomena
(Power)
(Temperature)
Physical Interactions
(Noise)
(Delay)
(Reliability)
…
Controller
Clock Freq.
Voltage, Clock Freq.

## Slide 114: Introduction to Energy Introspector
Energy Introspector (EI) is a simulation framework to facilitate the (selective) uses of different models and capture the interactions among microprocessor physics models.
Power Model Library
Reliability Model Library
Thermal Model Library
Coordinated Multi-Physics Interface
USER INTERFACE
compute_power();
compute_temperature();
INTERACTIONS
Model Library Wrappers
Microarchitecture
Description & Statistics
Available at www.manifold.gatech.edu
…

## Slide 115: Multi-Physics / Multi-Model Modeling
Different physical properties are modeled with different modeling tools.
Need to be able to easily integrate new models as they become available
  Costly when tightly integrated into microarchitecture simulation models
Power Modeling Tools
Thermal Modeling Tools
Reliability Modeling Tools
Delay Modeling Tools
McPAT (Cacti),
Orion (DSENT),
DRAMsim,
…
HotSpot,
3D-ICE,
TSI,
…
NBTI,
TDDB,
Electro-migration,
…
PDN,
Temperature Inversion,
…

## Slide 116: Physical Interaction Interface
Goals:
  Coordinated Modeling: The interface supports the modeling of different physical phenomena in the same domain of analysis by capturing their interactions; vs. trace-driven offline analysis
  Standardization: Different tools are integrated in the compatible way.
    Data definition is required for common, shared data.
    Different tools of the same data type can used in the identical way.
  Configurable Interface: Due to the integration of different tools, there must be a method to represent the different levels of processor components.
    Package | Floor-planning | Architecture/Circuit-level Blocks
  Data Synchronization: Data are shared between multiple tools.
  User Interface: User API is provided to trigger the calculation.
    The interface handles the data synchronization and interactions.
We introduce the Energy Introspector (EI) interface.

## Slide 117: COORDINATED MODELING: <Multiple physical phenomena modeled in the same domain of analysis>

## Slide 118: Energy | Power Modeling
Energy (or power) is characterized w.r.t. architectural activities.
Architecture
Component
(e.g., Data Cache)
(Read Counts = 100)
(Write Counts = 50)
(Miss counts = 20)
Architecture Simulation
Power Modeling Tool
Architecture Configuration
Physical Configuration
X
X
X
(Per-read Energy = 10pJ)
(Per-write Energy = 15pJ)
(Tag-read Energy = 3pJ)
Estimation
= 1nJ
= 0.75nJ
=0.06nJ
(Total Energy = 1.81nJ)
/ (Period = 1ns) = 1.81W
Sampling Interval
Leakage Power = 0.95W
+
Component Power = 2.76W
Processor Power = ∑ (Component Power)
* Numbers are randomly chosen to show an example.

## Slide 119: Thermal Modeling
Temperature is characterized at the package-level w.r.t spatiotemporal distribution of power (i.e., power density).
Architectural components are placed on the processor die (floor-planning).
The package is represented with layers of thermal grid cells.
A grid cell model
L2 Cache
Core
* Floor-plan is arbitrarily drawn to show an example.

## Slide 120: Reliability (Hard Failure) Modeling
Failures | Description
Electro-migration (EM), λEM | Directional transport of electrons and metal atoms in interconnect wires causes degradation and failure.
Time dependent dielectric breakdown (TDDB), λTDDB | Wearout of gate oxide caused by continued application of electric field leads to short between gate and substrate.
Hot carrier injection (HCI), λHCI | Electrons with sufficient kinetic energy overcomes the barrier to gate oxide and cause degradation.
Bias temperature instability (NBTI/PBTI), λBTI | Gradual degradation causes threshold voltage shift and eventually timing errors.
Stress migration (SM), λSM | Differences in the expansion rates of metals cause mechanical stress.
Thermal cycling (TC), λTC | Temperature cycle accumulates fatigue to materials.
Failure Rate = ∑ (λFAILURE)
Mean-time-to-failure (MTTF)= 1/Failure Rate
The failure rate is a function of operating conditions (i.e., voltage, temperature).

## Slide 121: Architecture-Level Physical Modeling
Abstract Representation of Architecture-Physics Interactions

## Slide 122: STANDARDIZATION: <Compatible Integration of Different Modeling Tools>

## Slide 123: Data Definition
Different models use different types and units of data.
The EI defines the modeled physical data.
// Basic Units
typedef uint64_t Count;
typedef double Meter;
typedef double Hertz;
typedef double Volt;
typedef double Kelvin;
typedef double Watt;
typedef double Joule;
typedef double Unitless;
typedef double Second;
// Activity Counters
class counter_t {
Count switching;
Count read;
Count write;
Count read_tag;
Count write_tag;
Count search;
void clear();
};
// Energy
class energy_t {
Joule total;
Joule dynamic;
Joule leakage;
void clear();
Joule get_total();
};
// Power
class energy_t {
Watt total;
Watt dynamic;
Watt leakage;
void clear();
Watt get_total();
};
power_t operator*(const energy_t &e, const Hertz &f);
power_t operator/(const energy_t &e, const Second &s);
// Dimension
class dimension_t {
Index layer_index;
char layer_name[LEN];
Meter left, bottom;
Meter width, height;
MeterSquare area;
void clear();
MeterSquare get_area();
};
// Grid
template <typename T>
class grid_t {
unsigned x, y, z;
unsigned count;
std::vector<T> element;
T& operator[](unsigned i)
...
};

## Slide 124: Integration of Modeling Tools (1)
Tools that model the same physical phenomena are categorized into the same library.
Each library defines the functions to be provided by the models.
  Energy Library:
    It calculates runtime energy/power dissipation w.r.t. architectural activity
    It estimates TDP power and area (if possible).
    Integrated models: McPAT, IntSim, to be integrated: DSENT, DRAMsim
  Thermal Library:
    It calculates transient/steady-state temperature w.r.t. power inputs.
    It requires floor-planning for the functional dies.
    It provides different levels of thermal data; grid, block, or point temp.
    Integrated models: HotSpot, 3D-ICE, to be integrated: TSI, Microfluidics
  Reliability Library:
    It calculates failure rate w.r.t. operation conditions (i.e., voltage, temp).
    Integrated model: Hard Failure

## Slide 125: Integration of Modeling Tools (2)
// Base Library Class
class model_library_t {
virtual ~model_library_t();
virtual bool update_library_variable(int Type, void *Value, bool IsLibraryVariable)=0;
virtual void initialize()=0;
};
// Energy Library Class
class energy_library_t : public model_library_t {
virtual ~energy_library_t();
virtual unit_energy_t get_unit_energy()=0;
virtual power_t get_tdp_power(Kelvin MaxTemperature)=0;
virtual power_t get_runtime_power(Second Time, Second Period, Counter_t Counter)=0;
virtual MeterSquare get_area()=0;
};
// Thermal Library Class
class thermal_library_t : public model_library_t {
virtual ~thermal_library_t();
virtual void calculate_temperature(Second Time, Second Period)=0;
virtual grid_t<Kelvin> get_thermal_grid()=0;
virtual Kelvin get_partition_temperature(Comp_ID ComponentID, int MappingType)=0;
virtual Kelvin get_point_temperature(Meter X, Meter Y, Index Layer)=0;
virtual void push_partition_power(Comp_ID ComponentID, power_t PartitionPower)=0;
virtual void add_pseudo_partition(std::string ComponentName, Comp_ID ComponentID)=0;
...
};

## Slide 126: Integration of Modeling Tools – Example
// Example: Integration of HotSpot
#include <HotSpot header files>
class thermallib_hotspot : public thermal_library_t {
~thermalib_hotspot();
void initialize() {
/* DEFINE A METHOD TO CREATE AND INITIALIZE HOTSPOT DATA STRUCTURES AND VARIABLES */
}
void update_library_variable(int Type, void *Value, bool IsLibraryVariable) {
/* DEFINE A METHOD TO DYNAMICALLY UPDATE HOTSPOT DATA STRUCTURES AND VARIABLES */
}
void calculate_temperature(Second Time, Second Period) {
/* DEFINE A METHOD TO ACCESS HOTSPOT DATA STRUCTURES AND CALCULATE TEMPERATURE */
}
void push_partition_power(Comp_ID ComponentID, power_t PartitionPower) {
/* UPDATE THE PARTITION (i.e., FLOOOR-PLAN) POWER FOR THE NEXT TEMP. CALCULATION */
}
Kelvin get_partition_temperature(Comp_ID ComponentID, int MappingType) {
/* RETRIEVE THE PARTITION (i.e., FLOOR-PLAN) TEMP. AFTER calculate_temperature(); */
}
...
};
Each integrated tool becomes a subclass of one of the model libraries.

## Slide 127: CONFIGURABLE INTERFACE: <A method to represent the different levels of processor components – from processor package to microarchitecture units>

## Slide 128: Abstract Representation of Processor Hierarchy
How can we flexibly mix and match models, microarchitecture components, and physical geometry?

## Slide 129: Processor Representation (1)

## Slide 130: Processor Representation (2)
Different physical phenomena are characterized and different levels of processor components.
The EI is comprised of pseudo components that can represent any processor components
  A pseudo component can represent a package, die, core, floor-plan block, etc.
  A pseudo component can be associated with an integrated modeling tool to characterize a physical phenomenon.
// Pseudo Component
class pseudo_component_t {
pseudo_component_t(Comp_ID ID, libEI::energy_introspector_t *EI, std::string Name,
libconfig::Setting *ConfigSetting, bool IsRemote);
Comp_ID id; // Integer ID
int rank; // MPI Rank (for parallel simulation)
std::string name; // String name
model_library_t *model_library; // Associated library tool
queue_t queue; // Data queue that stores computed results or shared data
libEI::energy_introspector_t *energy_introspector; // Pointer to main interface
libconfig::Setting *setting; // libconfig setting for this pseudo component
libEI::pseudo_component_t *superset; // A parent component in the processor hierarchy
std::vector<libEI::pseudo_component_t*> subset; // Child components
...
};

## Slide 131: DATA SYNCHRONIZATION: <Time synchronization and data sharing between library models>

## Slide 132: Data Synchronization (1)
for(all components)
EI->calculate_power(ComponentID,Time,Period,Counter,/*IsTDP*/false);
EI->calculate_temperature(PackageID,Time,Period,/*PowerSync*/true);
for(all components)
EI->calculate_power(ComponentID,Time,Period,Counter,/*IsTDP*/false);
EI->synchronize_data(packageID,Time,Period,EI_DATA_POWER); // Sync Power
EI->calculate_temperature(PackageID,Time,Period,/*PowerSync*/false);
Or, alternatively
The EI provides handles data synchronization across pseudo components.
Different data types have different synchronization method:
  Power, Area: added up from the bottom of the pseudo component tree.
  Temperature, Voltage, Clock Freq: applied identically to sub-components.

## Slide 133: Data Synchronization (2)
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
Pseudo Component
Data Queue
synchronize_data(EI_DATA_POWER);
∑ (sub-component Power);
∑ (sub-component Power);
Queue Error Detection:
Time discontinuous
Time outorder
Time overlap
Time invalid
Data duplicated
Data invalid
Data type invalid
Invalid pseudo component

## Slide 134: Data Manipulation
Each pseudo component includes data queues to store computed results or shared data.
Data are of discrete time, and thus associated with time, period information.
  Closed Queue:
    This queue type is used for periodically calculated and sampled data such as power, temperature, etc.
    Data are continuous to the left; valid interval = (time-period, time]
  Open Queue: This queue type is used for aperiodically controlled data such as voltage, clock frequency, etc.
    Data are continuous to the right; valid interval = [time, unknown)
The insertion of data triggers the callback function of the library model (if any) to update dependent variables and states.
Simulation Progress
Time = 0.1sec
Period = 0.1sec
Time = 0.2sec
Period = 0.1sec
Time = 0.3sec
Period = 0.1sec
Sampling & Calculation

## Slide 135: Data Queue Structure
Each pseudo component includes data queues to store computed results or shared data.
// Base Queue
class base_queue_t {
virtual ~base_queue_t();
void reset();
int get_error();
unsigned size; // Queue length
int error; // Error code
};
// Individual Data Queue
template <typename T>
class data_queue_t : public base_queue_t{
~data_queue_t();
void reset();
void push(Second Time, Second Period, T Data);
void overwrite(Second T, Second P, T D);
T pull(Second T, Second P);
int queue_type; // Open / Close Queue
int data_type; // Data Type
std::map<data_time_t,T> queue;
};
// Pseudo Component Data Queue
Class queue_t {
~data_queue_t();
template <typename T>
void create(unsigned QueueLength,
int DataType, int QueueType);
template <typename T>
void push_back(Second Time, Second Period,
int DataType, T Data);
template <typename T>
void overwrite(Second Time, Second Period,
int DataType, T Data);
template <typename T>
T get(Second Time, Second Period,
int DataType);
void register_callback(model_library_t *Lib,
bool(model_library_t::*update_library_variable)
(int,void*,bool));
void callback(int DataType, void *Data);
int get_error();
void reset();
std::map<int,base_queue_t*> queue;
};

## Slide 136: INPUT CONFIG & USER INTERFACE: <EI Configuration and User API>
Package
(thermal)
Core0
(Reliability)
Core1
(Reliability)
Core2
(Reliability)
Core3
(Reliability)
Shared L2
(Energy)
Inst Cache
(Energy)
BTB
(Energy)
Inst Decoder
(Energy)
…
(Energy)
ALU
(Energy)
LD/STQ
(Energy)
* Within () shows the modeled library at each pseudo component.
Thermal Library = 3D-ICE
Reliability Library = Hard Failures
Energy Library = McPAT

## Slide 137: Input Configuration
The EI uses the libconfig to parse the input file.
// Example
component: {
package: {// package
library: {
model = “3d-ice”;
ambient_temperature = 300.0;
grid_rows = 100;
/* 3D-ICE PARAMETERS */
};
component: {
core0: {// package.core0
  library: {
  model = “none”;
  voltage = 0.8;
  clock_frequency = 2.0e9;
  /* COMMON PARAMETERS OF core0 */
  };
  component: {
  data_cache: {
  };
  };
}; // package.core0
};
}; // package
};
// Continued with core.data_cache
component: {
data_cache: {// package.core0.data_cache
library: {
model = “mcpat”;
energy_model = “array”;
energy_submodel = “cache”;
line_sz = 64;
assoc = 4;
/* MCPAT PARAMETERS */
/* NO NEED TO REDEFINE voltage */
};
}; // package.core.data_cache
inst_dec: {// package.core0.inst_dec
library: {
model = “mcpat”;
energy_model = “inst_decoder”;
x86 = true;
/* MCPAT PARAMETERS */
};
}; // package.core0.inst_dec
...
};

## Slide 138: User API Example (1)
The simulator creates the Energy Introspector.
Each manifold model has the pointer to the Energy Introspector.
// Example – Serial Simulation
/* MAIN FUNCTION: CREATE AND CONFIGURE THE ENERGY INTROSPECTOR */
energy_introspector_t *ei = new energy_introspector_t(“input.config”); // Create EI
ei->configure(); // Configure EI
...
/* CONNECT EI INTERFACE – SERIAL SIMULATION */
Core_t *core = Component :: GetComponent<core_t>(ManifoldCoreID);
core->connect_EI(ei);
core->set_sampling_interval(0.0001);
...
Manifold :: Run();
...

## Slide 139: User API Example (2)
The EI provides several API functions to use the models.
/* WITHIN A MANIFOLD MODEL */
Comp_ID package_id, core_id, data_cache_id;
...
/* IDs ARE REQUIRED FOR ALL COMPONENTS WHERE DATA ARE MONITORED */
counter_t data_cache_counter; // Data cache counter
...
/* COUNTERS ARE DEFINED FOR ALL COMPONENTS WHERE POWER IS CHARACTERIZED */
void core_t::connect_EI(energy_introspector_t *ei) {
energy_introspector = ei;
// Get the pseudo component ID of modeled processor components
package_id = energy_introspector->get_component_id(“package”);
assert(package_id != INVALID_COMP_ID);
...
}
void core_t::tick() {
if(NowTicks() % sampling_interval == 0) {
/* ARCHITECTURE SIMULATION IS PERFORMED, AND COUNTERS ARE COLLECTED FOR DATA CACHE */
energy_introspector->calculate_power(data_cache_id,time,period,data_cache_counter);
/* calculate_power() IS CALLED FOR ALL COMPONENTS WHERE POWER IS CHARACTERIZED */
energy_introspector->calculate_temperature(time,period,/*PowerSync?*/true);
int err; Kelvin core_temp; // Data are already sync’ed
err = energy_introspector->pull_data(core_id,time,period,EI_DATA_TEMPERATURE,&core_temp);
}
}

## Slide 140: DEMONSTRATION <Architecture-physics co-simulation via Manifold and Energy Introspector>
// Trace file from the simulation
time= 124.0 | core0
instantIPC= 0.997120 , avgIPC= 1.008513
power= 2.195946 W (dynamic= 1.299701 W, leakage= 0.896246 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 332.3, failure_rate= 1.934528e-11 (MTTF= 1.269645)
time= 124.0 | core1
instantIPC= 1.088155 , avgIPC= 1.089841
power= 2.325650 W (dynamic= 1.418857 W, leakage= 0.906793 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 335.9, failure_rate= 2.228109e-11 (MTTF= 1.102353)
time= 124.0 | core2
instantIPC= 1.372630 , avgIPC= 1.239406
power= 2.698654 W (dynamic= 1.791860 W, leakage= 0.906793 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 335.8, failure_rate= 2.189546e-11 (MTTF= 1.121768)
time= 124.0 | core3
instantIPC= 1.124560 , avgIPC= 1.050577
power= 2.361293 W (dynamic= 1.465048 W, leakage= 0.896246 W, area= 5.28mm^2)
clk= 2.000 GHz, temp= 333.0, failure_rate= 1.958338e-11 (MTTF= 1.254208)

## Slide 141: PARALLEL INTERFACE: <Parallel Simulation via MPI interface>
Manifold Process 1
Package
(thermal)
Core0
(Reliability)
Core1
(Reliability)
Core2
(Reliability)
Core3
(Reliability)
Shared L2
(Energy)
EI Process 1
EI Process 0
Core0
Core1
Core2
Core3
Shared L2
Manifold Process 0
Network
MPI Inter-communicator

## Slide 142: Parallel EI Configuration
The EI supports parallel simulation via the MPI interface.
The pseudo component hierarchy can be partitioned into multiple MPI processes.
// Example – Rank0
component: {
package: {// package
library: {
model = “3d-ice”;
ambient_temperature = 300.0;
grid_rows = 100;
/* 3D-ICE PARAMETERS */
};
component: {
core0: {// package.core0
  remote = true;
}; // package.core0
core1: {// package.core1
  remote = true;
}; // package.core1
core2: {// package.core2
  model = “none”;
}; // package.core2
...
};
}; // package
};
// Example – Rank1
component: {
package: {// package
library: {
remote = true;
};
component: {
core0: {// package.core
  library: {
  model = “none”;
  voltage = 0.8;
  clock_frequency = 2.0e9;
};
...
}; // package.core
};
}; // package
};

## Slide 143: Parallel API Example (1)
The MPI process creates the Energy Introspector.
// Example – Parallel Simulation
/* MAIN FUNCTION: CREATE AND SPLIT THE MPI COMMUNICATOR FOR MANIFOLD AND EI */
MPI_Comm INTER_COMM, LOCAL_COMM;
MPI_Comm_split(MPI_COMM_WORLD,(MyRank<Manifold_NPs),Rank,&LOCAL_COMM);
MPI_Intercomm_create(LOCAL_COMM,0,MPI_COMM_WORLD,MyRank<Manifold_NPs?
Manifold_NPs:0,1234,&INTER_COMM);
/* CREATE AND CONFIGURE THE ENERGY INTROSPECTOR */
energy_introspector_t *ei = new energy_introspector_t(“input-rank0.config”,
INTER_COMM,LOCAL_COMM);
ei->configure(); // Configure EI
...
Manifold :: Init(argc,argv,&LOCAL_COMM); // Manifold runs within its MPI communicator
...
/* INSTANTIATE EI CLIENT – PARALLEL SIMULATION */
Core_t *core = Component :: GetComponent<core_t>(ManifoldCoreID);
core->connect_EI(&INTER_COMM, Rank);
core->set_sampling_interval(0.0001);
...
Manifold :: Run();
...

## Slide 144: Parallel API Example (2)
The EI client is used to communicate over MPI processes.
/* WITHIN A MANIFOLD MODEL */
void core_t::connect_EI(MPI_Comm *InterComm, int EIRank);
// Create EI client interface
EI_client_t *EI_client = new EI_client(InterComm,EIRank);
// Get the pseudo component ID of modeled processor components
package_id = EI_client->get_component_id(“package”);
assert(package_id != INVALID_COMP_ID);
...
}
void core_t::tick() {
if(NowTicks() % sampling_interval == 0) {
/* ARCHITECTURE SIMULATION IS PERFORMED, AND COUNTERS ARE COLLECTED FOR DATA CACHE */
EI_client->calculate_power(data_cache_id,time,period,data_cache_counter);
/* calculate_power() IS CALLED FOR ALL COMPONENTS WHERE POWER IS CHARACTERIZED */
EI_client->calculate_temperature(time,period,/*PowerSync?*/true);
Kelvin core_temp; power_t core_power; // Data are already sync’ed
int err = EI_client->pull_data(core_id,time,period,EI_DATA_POWER,&core_power);
err = EI_client->pull_data(core_id,time,period,EI_DATA_TEMPERATURE,&core_temp);
}
}

## Slide 145: EI: Summary
The Energy Introspector is an enabler for architecture-physics exploration.
Any new models can be incorporated into the interface, and we plan to add more models.
For an access to the latest EI:
svn co https://svn.ece.gatech.edu/repos/Manifold/trunk/code/models/energy_introspector/

## Slide 146: Outline
Introduction
Execution Model and System Architecture
Multicore Emulator Front-End
Component Models
  Cores
  Network
  Memory System
Building and Running Manifold Simulations
Physical Modeling: Energy Introspector
Some Example Simulators

## Slide 147: What can Manifold Enable?
Manifold enables cross-disciplinary evaluations
Applications  Power  Thermal  Cooling
Multi-scale simulation  cycle-level to functional
Tradeoff studies
Performance
Reliability
Energy/Power
www.commons.wikimedia.org
imaging1.com
Large Graphs

## Slide 148: Some Example Simulators
Power capping studies
Reliability studies
Workload  Cooling interaction

## Slide 149: Power Capping: Simulation Model
Power Targets
Controller gain is adjusted every 5 ms
Each core has its own core and power budget – two OOO and two IO cores.

## Slide 150: Power Capping Controller
High fixed-gain controller over-reacts to high power cores, whereas low fixed-gain control is slow to react to low power cores.
N. Almoosa, W. Song, Y. Wardi, and S. Yalamanchili, “A Power Capping Controller for Multicore Processors,” American Control Conf., June 2012.
New set point

## Slide 151: Throughput Regulation: Adaptive
High fixed-gain controller over-reacts to high power cores, whereas low fixed-gain control is slow to react to low power cores.
N. Almoosa, W. Song, Y. Wardi, and S. Yalamanchili, “Throughput Regulation on Multicore Processors via IPA,” 2012 IEEE 51st Annual Conference on Decision and Control (CDC)

## Slide 152: Adaptation to Aging and Reliability
64-core asymmetric processor floor plan
Failure probability comparison between per-core race-to-idle executions (left) and continuous low-voltage executions (right)
Transient race-to-idle executions vs. continuous executions
LVF: Low Voltage Frequency
HVF: High Voltage Frequency
NVF: Nominal Voltage Frequency

## Slide 153: Workload-Cooling Interaction
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
FE
SCH
DL1
INT
FPU
Nehalem-like, OoO cores;
3GHz, 1.0V, max temp 100◦C
DL1: 128KB, 4096 sets, 64B
IL1: 32KB, 256 sets, 32B, 4 cycles;
L2 & Network Cache Layer:
L2 (per core): 2MB, 4096 sets, 128B, 35 cycles;
DRAM: 1GB, 50ns access time (for performance model)
Ambient:
Temperature: 300K
Thermal Grids: 50x50
Sampling Period: 1us
Steady-State Analysis
2.1mm x 2.1mm
8.4mm x 8.4mm
16 symmetric cores
CORE DIE
MICROFLUIDICS
SRAM
Coolant/Configuration | A | B | C
Flow rate (ml/min) | 7 | 42 | 84
Top Heat Coeff (W/um2-K) | 2.05e-8 | 5.71e-8 | 8.01e-8
Bot. Heat Coeff (W/um2-K) | 1.69e-8 | 4.72e-8 | 6.63e-8

## Slide 154: Impact of Flow Rate & Workload on Energy Efficiency
Chart: nJ/inst
| barnes | canneals | fft | ocean-c | radix
A | 2.47 | 2.37 | 2.24 | 2.38 | 2.63
B | 2.32 | 2.21 | 2.15 | 2.16 | 2.26
C | 2.22 | 2.12 | 2.13 | 2.14 | 2.17
Chart: MIPS/W
| barnes | canneals | fft | ocean-c | radix
A | 404.8583 | 421.9409 | 446.4286 | 420.1681 | 380.2281
B | 431.0345 | 452.4887 | 465.1163 | 462.963 | 442.4779
C | 450.4505 | 471.6981 | 469.4836 | 467.2897 | 460.8295
Memory bound applications benefit more than computation bound applications
Overall energy improvement
  4.9%-17.1% over 12X increase in flow rate
  4.0%-14.1% over 6X increase in flow rate
Does not include pumping power

## Slide 155: 3D Stacked ICs Structure Model
3D stacked ICs structure
Simplified structure
Conduction FE model and temperature results
heff=562.4 W/m2*K
Effective heat transfer coefficient is obtained by FE model on the left:
Z. Wan et. al., IEEE Therminic 2013, Berlin, 25. -27. Septemeber 2013 (accepted)

## Slide 156: Case Study with Different Microgap Configurations
Microgap configurations
Configuration 1: One microgap
Configuration 2: Two microgaps
Temperature results: One microgap, logic tier at bottom and memory tier on the top
Pump power:0.03 W | Configuration |  |  | Tmax,logic (℃) | Tmax,memory (℃)
 | Micro-gap | Top | Bottom |  | 
Case 1 | 1 | M | L | 93.1 | 82.2
Case 2 | 1 | L | M | 114.9 | 77.1
Case 3 | 2 | M | L | 87.7 | 54.8
Case 4 | 2 | L | M | 72.7 | 58.3
Logic tier
Memory tier
Results for different cases

## Slide 157: Summary
Not to provide a simulator, but
Composable simulation infrastructure for constructing multicore simulators, and
Provide base library of components to build useful simulators
Novel Cooling Technology
Thermal Field Modeling
Power Distr. Network
Power Management
μarchitecture
Algorithms
Microarchitecture
and Workload Execution
Power Dissipation
Thermal Coupling
and Cooling
Degradation
and Recovery
www.manifold.gatech.edu